## Slide 1: Checkpoint Project #2
Dual Axis Motion Control – Pin Spotter

## Slide 2: Requirements:
Visualization:
  Splash/Loading Screen
  All text in text groups
  Machine status shown on all screens
  Global Layers
  Alarms and Reactions
  Units & Limits
  All best practices followed.
Program
  Dual-axis motion (camming or gearing)
  Slaves home to a specific position (12:00)
  Allow user to input an offset from slave’s homing position
  Change speed during runtime from Vis
    Requires user confirmation
  Correct units & period settings
    Consider real life and your hardware
  Focus on error handling, diagnostics, and optimization.

## Slide 3: Pin Spotter:
5x
The pin spotter drives a series of pins through a pad of insulation, binding the insulation to the duct panel below.
Conveyor Motor (Master): Moves a duct panel along at a steady speed.
Pin Spotter Motor (Slave): Lowers the Pin Spotter tool onto the duct panel, then raises it to reload the pin. This process is repeated 5 times per panel while the panel moves below the pin spotter.

## Slide 4: Control Task States:
INIT
READY
MOVE_PANEL
Main.Status.Ready
Main.Cmd.Start
Main.Cmd.Stop AND Main.Status.Ready
ERROR
Alarm.Error = TRUE
Alarm.Error = FALSE
Main.Cmd.Stop AND NOT Main.Status.Ready
INSERT_PINS
Main.Status.PanelInPosition
Main.Status.PinsComplete

## Slide 5: Control Task States:
INIT
ERROR
Alarm.Error = TRUE
Alarm.Error = FALSE
READY
RESET
POSITION_PANEL
INSERT_PINS

## Slide 6: Axis Task States:
INIT
POWER
HOME
READY
ERROR
TUNE
RUN
Axis.Status.Active AND
NOT Axis.Status.PowerOn
Axis.Status.PowerOn AND
NOT Axis.Status.Homed
Axis.Status.Homed
Axis.Status.PowerOn
Axis.Cmd.Autotune
Axis.Status.TuneComplete
Axis.Status.PowerOn AND
Axis.Status.Homed
MainCtrl.Cmd.Run = TRUE
MainCtrl.Cmd.Run = FALSE
COUPLE
Axis.Status.Coupled
Axis.Status.PowerOn AND
Axis.Status.Homed AND
NOT Axis.Status.Coupled
Axis.Cmd.Power
Axis.Cmd.Home
Axis.Cmd.Couple
Axis.Cmd.MoveVel
Axis.Status.Error = TRUE
Axis.Status.Error = FALSE

## Slide 7: Software Requirements:
Libraries:
  Standard
  Acp10main
  Acp10par
  Acp10_MC
  NcGlobal
  MpAxis
  MpBase
Function Blocks:
  Motion
    MpAxisBasic
    MpAxisCoupling
    MC_GearInPos
    MC_GearOut
  Alarm
    MpAlarmXCore
Built in Types:
  Motion
    MpAxisCouplingParType
    MpAxisBasicInfoType
    MpAxisBasicParType
    ACP10AXIS_typ
  Alarm
    MpAlarmXListUIConnectType
    MpComIdentType
    MpAlarmXListUISetupType
    MpAlarmXListUI
Tasks:
  MainCtrl
  MotionCtrl
  AlarmCtrl
  VisCtrl

## Slide 8: Main Control Structures:
MainCtrl_type
  Axis_type[0..2]
    [VirtualMaster, PinSpotter, Conveyor]
  MpAxisBasic[0..2]
  ACP10AXIS_typ[0..2]
  MpAxisCoupling
  MainState_enum
  Error_type
  Alarm_type
  MainCmd_type
  MainStatus_type
  Counts_type
MainState_enum
  INIT
  READY
  RUN
  ERROR
Error_type
  ErrorActive
  ErrorSetID
  ErrorResetID
  ErrorName
  LastState
  ErrorAcknowledgeID
Alarm_type
  MpComIdentType
  MpAlarmXListUIConnectType
MainCmd_type
  Start
  Stop
MainStatus_type
  Ready
Counts_type
  PanelsFinished
  PinsPlacedCurrent
  PinsPlacedTotal

## Slide 9: Motion Structures:
Axis_type
  AxisState_enum
  Coupling_type
  Cmd_typ
  Status_type
  Par_type
AxisState_enum
  INIT
  POWER
  HOME
  COUPLE
  READY
  RUN
  TUNE
  ERROR
Coupling_type
  Parameters
  CamCmd
Cmd_type
  MoveAbsolute
  MoveAdditive
  MoveVel
  JogPos
  JogNeg
  Home
  Power
  ErrorReset
  Stop
  Autotune
  Initialize
Status_type
  PowerOn
  Active
  Homed
  Velocity
  Info
  Stopped
  MoveActive
  InVelocity
  Position
  Error
  TuningDone
  Ready
  PanelInPosition
Par_type
  BasicPars

## Slide 10: Vis Structures:
Vis_type
  Page_enum
  VisStatus_type
  VisCmd_type
  Locking_type
  Visibility_type
  VisCounts_type
  MotorConfig_type
Page_enum
  Splash
  Main
  Config
  Alarms
  Diagnostics
VisStatus_type
  State_enum
VisCmd_type
  Run
  Init
  Tune
  Update
Locking_type
  BeltMoving
  NotReady
Visibility_type
  ShowAlarmDialog
VisCounts_type
  PanelsFinished
  PinsPlacedCurrent
  PinsPlacedTotal
MotorConfig_type
  Speed
  Offset

## Slide 11: Cam Profile:
1 Panel per 1m of belt.
1 Panel is 0.7m wide.
Panel is centered in each 1m section of belt.
Pins begin 0.1 from the leading edge, and are placed at 0.1 intervals.
Belt
Panel
1m
0.7m
0.15m
0.1m
0.5m
0.1m
0.25m
0.5m
Motor Config: (?)
Virtual Master
  Periodic Linear
  Units: mm
  Period: 1000mm
  Reference distance: 1000mm
Slave1 (Pin spotter tools)
  Limited Linear
  Units mm
  Lower Limit: -5mm
  Upper Limit: 100mm
Motor1 (Conveyor)
  Linear
  Units: mm
  Period: 1000mm
  Reference distance: 1000mm

## Slide 12: Cam Profile:

## Slide 13: Shared Layer: GlobalNavStatusLayer
Main
Config
Diag
Alarm
MachineStatus
ConveyorMotorStatus
PinSpotterMotorStatus
DateTime

## Slide 14: Shared Layer: MotorStatusLayer
Conveyor Power
Conveyor Homed
Conveyor Moving
Conveyor Error
Pin Power
Pin Homed
Pin Moving
Pin Error

## Slide 15: Shared Layer: AlarmLayer
ERROR

## Slide 16: Splash Page
Conveyor Power
Conveyor Homed
Conveyor Moving
Conveyor Error
Pin Power
Pin Homed
Pin Moving
Pin Error

## Slide 17: Main Page
Main
Config
Diag
Alarm
Machine: READY
Conveyor: READY
PinSpotter: READY
DateTime
Belt Position
Panel Position
Panel Done Count
Tool Position
Conveyor Power
Conveyor Homed
Conveyor Moving
Conveyor Error
Pin Power
Pin Homed
Pin Moving
Pin Error
Pins Placed
Speed

## Slide 18: Config Page
Main
Config
Diag
Alarm
Machine: READY
Conveyor: READY
PinSpotter: READY
DateTime
Tune
Set Pin Home
Conveyor Power
Conveyor Homed
Conveyor Moving
Conveyor Error
Pin Power
Pin Homed
Pin Moving
Pin Error
Pin Offset